## Slide 1
Metrology Design
Project Name: J510
Part Number & Rev：
160-06631-01-01
Vendor：
MAGSOUND
Date：
2025/01/14

## Slide 2
Cover sheet Page 1
Content Page 2
history List Page 3
Measurement Equipment Page 4-9
Measurement Fixture List Page 10
Bom List Page 11
Details for Each Measurement Page 12-22

## Slide 3
MTD | J510 | Measurement Equipment Details
Name: KEYENCE
Manufacturer:
KEYENCE
Model:
IM-7101
Range:
Φ100x200mm (Wide), Φ25x125mm (High)
Accuracy:
±0.001mm

## Slide 4
MTD | J510 | Metrology Details
FAI | SPC | Specification | Description | Method | Fixture | In-Process | Cross check
1 | A | 3*2.00±0.10 | Thickness | HG |  | No | Guo Teng
2 | B | 3*2.85±0.10 | Width | Keyence |  | No | Guo Teng
3 | C | 14.20±0.10 | Length | Keyence |  | No | Guo Teng
4 | D | 2*30.96°±3.00° | Angle | Keyence |  | No | Guo Teng

## Slide 5
Mono Magnet Thickness
FAI 1/SPC A: 3*2.00±0.10 CPK
1. Measurement Method：HG
2. Fixture：/
3. Measurement status：Free
4. Measurement procedure：
1. 将产品如下图平放大理石平台上
2. 将高度规测针在大理石平台上A1点归零
3. 测量产品厚度并记录数值
[测量示意图]